## Slide 1: Sparse Matrix-Vector Multiply on the Keystone II Digital Signal Processor
Yang Gao, Fan Zhang and Dr. Jason D. Bakos
2014 IEEE High Performance Extreme Computing Conference(HPEC ‘14)

## Slide 2: Heterogeneous Computing on Embedded Platforms
GPU/FPGA/DSP(KeyStone)
ARM + Embedded GPUs/FPGA/DSP(KeyStone II)
 | Embedded GPU |  |  | FPGA | DSP
Platforms | PowerVR SGX 544MP3 | PowerVR G6430 | GK20A (Kepler) | Zynq-7000 | KeyStone II
 | Exynos 5 Octa | Apple A7 | Tegra K1(Jetson) | 7Z045 | TCI6638
Theoretical Peak Performance (Gflops) | 51.1 | 115.2 | @864 MHz 331 | 65 | @1.35GHz 172.8
Notes: Summarize the table,

## Slide 3: Key Features of KeyStone II
In-order execution, static scheduled VLIW processor
8 symmetric VLIW cores with SIMD instructions, up to 16 flops/cycle
No shared last level cache
6MB on-chip shared RAM (MSMC)
L1D and L2 can be configured as cache, scratchpad, or both
DMA engine for parallel loading/flushing scratchpads
High performance, Low power consumption design
Notes: Unique processor, hard to program

## Slide 4: VLIW and Software Pipeline
for i = 0 to n
$1 = load A[i]
add $2,$2,$1
A[i] = store $2
endfor
A
L
S
Regular Loop
Load 3 cycles
Add 3 cycles
Store 1 cycles
VLIW Software
Pipelined Loop with static scheduler
L
S
L
S
L
S
7 cycles
3
cycles
After Schedule
Out-of-order Processor with dynamic scheduler
A
A
A
Software Pipeline Restrictions:
Not friendly to conditional code inside loop body
Register Limitations
Rely on compiler to exert the optimization in low level
Notes: Practical limitation, branches, register, assembly(parallel not happen obviously, lower level than C), 3 cycles add

## Slide 5: DSP Memory Hierarchy
1024K Level 2 SRAM
Cache
SPRAM
 | Size (KB) | Cache Capacity(KB)
L1P | 32 | 0/4/8/16/32
L1D | 32 | 0/4/8/16/32
L2 | 1024 | 0/32/64/128/256/512/1024
MSMC | 6144 | 0
Cache
SPRAM
Cache
SPRAM
Notes: Text book style simple cache
Cache could also be SPM
Share memory could be SPM

## Slide 6: SPM Method and Double Buffer
Load 0
Load 1
Compute 0
Load 0
Compute 1
EDMA
DSP
Corepac
Time
Compute 0
Notes: 2 stages could be pipelined
Loop tilling + double buffer is basic optimization strategy in the DSP platform.

## Slide 7: Sparse Matrices
We evaluated the Keystone II using a SpMV kernel
Sparse Matrices can be very large but contain few non-zero elements
Compressed formats are often used, e.g. Compressed Sparse Row (CSR)
1 | -1 | 0 | -3 | 0
-2 | 5 | 0 | 0 | 0
0 | 0 | 4 | 6 | 4
-4 | 0 | 2 | 7 | 0
0 | 8 | 0 | 0 | -5
val | (1 | -1 | -3 | -2 | 5 | 4 | 6 | 4 | -4 | 2 | 7 | 8 | -5)
col | (0 | 1 | 3 | 0 | 1 | 2 | 3 | 4 | 0 | 2 | 3 | 1 | 4)
ptr | (0 | 3 | 5 | 8 | 11 | 13) |  |  |  |  |  |  | 
Notes: 3 arrays, one simple example

## Slide 8: Sparse Matrix-Vector Multiply
Code for y = Aax + by
  row = 0
  for i = 0 to number_of_nonzero_elements do
    if i == ptr[row+1] then row=row+1, y[row]*=beta;
    y[row] = y[row] + alpha * A[i] * x[col[i]]
  end
reduction
indirect indexing
Low arithmetic intensity
(~3 flops / 24 bytes)
Memory bound kernel
conditional execution
Notes: Indirect indexing: load dependence.
Utilization 6ALU+2L/S
Dependency
Software pipelining

## Slide 9
for i = elements assigned to current core
val array
col array
x array
ptr array
y
array
i
row
if ptr[row] = i then
row = row+1
y[row]y[row]*β
endif
y[row]y[row]+acc
α*val*x
prod buffer
i
DDR arrays
val buffer
col buffer
acc  acc+prod[i]
if ptr[row] = i then
row = row+1
y[row]y[row]*β+acc
endif
Product Loop
Accumulation Loop
if(ptr[row+1]-ptr[row])>K
acc  acc+prod[i+1]
if ptr[row] = i then
row = row+1
y[row]y[row]*β+acc
endif
acc  acc+prod[i+k]
if ptr[row] = i then
row = row+1
y[row]y[row]*β+acc
endif
Manually Unrolled Loop
Loop Fission
DMA Double buffer
acc  acc+prod[i]
acc  acc+prod[i+1]
…
acc  acc+prod[i+k]
Adaptive Row Pointer
Predicate Instruction
Assembly Optimization
DDR arrays
DMA Circular buffer
ptr buffer
y
buffer

## Slide 10: Buffer Location and Performance
Buffer
val
col
ptr
y
prod
Locations
L2
MSMC
cache
map?
L1
L2
MSMC
cache
Notes: Data is provided by TI, information is public
Data path is decided by allocation

## Slide 11: Matrix
Tri-diagonal
N-diagonal
3, 151
2, 4, 0, 0, 0, 0
5, 4, 7, 0, 0, 0
0, 6, 2, 4, 0, 0
0, 0, 3, 10, 1, 0
0, 0, 0, 4, 6, 8
0, 0, 0, 0, 2, 12

## Slide 12: Buffer Location and Performance
Non-zeros per row | val | col | ptr | y | prod | Gflops | Norm. Perf | Note
3 | S S L2 C | L2 L2 L2 C | L2 L2 C C | L2 L2 C C | L1 L2 S C | 2.26 1.84 1.23 1.44 | 1.57 1.28 0.85 1 | Best Median Worst2 All cache
151 | L2 S C C | S C C C | L2 L2 C C | L2 L2 C C | L2 S L2 C | 3.76 3.55 2.66 2.51 | 1.50 1.41 1.06 1 | Best Median Worst2 All cache
L1: level 1 SPRAM, L2:level 2 SPRAM, S:MSMC, C:cache
1: The results are normalized to the all cache configuration
2: The worst amongst the configurations with SPRAM
Notes: Matrix: synthetic matrix, dense and sparse
Variance, mapping is important
Cache is not worst.
Not the kernel, the input data is also important

## Slide 13: Matrix
Tri-diagonal
N-diagonal
3, 151
University of Florida sparse matrix collection
Matrix Market
2, 4, 0, 0, 0, 0
5, 4, 7, 0, 0, 0
0, 6, 2, 4, 0, 0
0, 0, 3, 10, 1, 0
0, 0, 0, 4, 6, 8
0, 0, 0, 0, 2, 12

## Slide 14: Testing Platforms
 | Intel i7 3770K MKL | NVIDIA GTX 680 cuSparse | NVIDIA Tegra K1 cuSparse | TI 6638K2K
Arch | Ivy Bridge | Kepler | Kepler | KeyStone II
Memory B/W(GB/s) | 25.6 | 192.3 | 17.1 | 12.8
SPRAM KB/core | n/a | 64/641 | 64/641 | 32/1024/7682
Single Precision Peak Throughput (Gflops) | 448 | 3090 | 365 | @1.35GHz 172.8(DSP) 44.8(ARM)
TDP(W) | 77 | 195 | ~10 | ~15
Register file/allocable share memory or L1
L1 SRAM / L2 SRAM / MSMC per core
Notes: Very different in M/B and performance

## Slide 15: Close Comparison to NVIDIA Tegra K1
 | Tegra K1 | TI 6638K2K
Architecture | Cortex A15 + Kepler GPU | Cortex A15 + Keystone II DSP
CPU | 4 Cores, 2.2 GHz 32K+32K L1 2M L2 | 4 Cores, 1.4 GHz 32K+32K L1 4M L2
Co-processor | 192 CUDA cores @864 MHz 331 Gflops (SP peak) | 8 DSP cores @ 1.35GHz 172.8 Gflops (SP peak)
Memory Bandwidth | 17.1 GB/s(DDR3-2133) | 12.8 GB/s(DDR3-1600)
Power | ~ 10 W | ~ 15 W
Notes: Most recent GPU

## Slide 16: Performance Comparison vs. Nvidia TK1

## Slide 17: Performance Comparison

## Slide 18: Kernel/Memory Efficiency
efficiency =
observed performance/((Arithmetic Intensity) X (Memory Bandwidth))

## Slide 19: Conclusion
Significant performance gain with loop tuning and SPM optimizations
Despite the mobile GPU’s higher theoretical SP performance and memory bandwidth, the DSP outperforms it with our SpMV implementation.
Auto-decided SPM buffer allocation/mapping by a model of data access pattern.
Notes: *carefully loop tuning and scratchpad optimization
*higher performance than Tegra, despite the GPU’s spec is better
*the mapping optimization could be abstracted by a model, auto allocation

## Slide 20: Q & A